## Slide 1: Survey of Side-Channel Vulnerabilities for Short-Range Wireless Communication Technologies
Dr. Shannon Beck, Dr. Manohar Raavi, Caleb Dale, Kaija Weishalla, Brennan Worrell

## Slide 2: Survey Paper Outline
Motivation
Side Channels
For each protocol:
  Description
  Vulnerabilities
  Mitigations
Protocols discussed:
  RFID
  Bluetooth
  ZigBee
  Qi
  Li-Fi
Conclusion

## Slide 3: Motivation
Undergraduate research
Support background knowledge of wireless power charging capstone
First larger-scale paper
Skills focus:
  Research
  Discussion of source credibility
  Use and integrate knowledge from across various source types: papers, cybersecurity blogs, CVEs, standards documents
  Citation work
  Gain knowledge of research area
  Peer review and feedback

## Slide 4: Side Channels
Side Channel:
Gain information by analyzing unintended outputs or behaviors instead of directly accessing the system itself
Exploit physical characteristics of system rather than directly targeting its cryptographic algorithms or software vulnerabilities.
  EM spectrum for paper, exception of Li-Fi with light spectrum

## Slide 5: RFID / NFC
Notes: Tags / card: https://electronics.howstuffworks.com/near-field-communication.htm
Book: https://www.leghorngroup.com/rfid-labels-for-books/

## Slide 6: RFID
Radio Frequency Identification
Uses microchip tags and scanners to enable
device identification and tracking
Close range wireless communication, includes NFC
Uses include:
  medical equipment [48], inventory [49] and supply chain management [50], credit cards [51]
Widely used, users require confidence
  Transmit sensitive information (passports, credit cards, physical access etc.)

## Slide 7: RFID Vulnerabilities
Attacks and Mitigations:
  Tear-off attack – physical security
  Eavesdrop / skim (within 10 cm) - use encryption [7][9]
  Cloning - Detect duplicate (cloned) or counterfeit RFID tags [11]
  Incorrect use of cryptography
General mitigations: Cybersecurity best practices
  Implement secure key management practices to protect the cryptographic keys
  Conduct regular security audits
  Install firmware and software updates to address known vulnerabilities
Notes: Correct use of cryptography algorithms, such as the 128-bit AES cipher with randomization enabled is a commonly-used practice to counteract side-channel attacks [7], [9]. Detection of duplicate (cloned) or counterfeit RFID tags [11]. Cyber best practices apply here: implement secure key management practices to protect the cryptographic keys, conduct regular security audits, and install firmware and software updates to address known vulnerabilities

## Slide 8: Bluetooth Devices
Notes: Headset: https://a.co/d/6SUfdrY
BLE Arduino: https://store-usa.arduino.cc/products/bluetooth-low-energy-4-0-module-hm-10

## Slide 9: Bluetooth
Below Wi-Fi, most prevalent wireless communication protocol
Examples: headphones, keyboards, vehicles, phones
BLE (Bluetooth Low Energy)
  Lower range
  Higher transfer rate
  Lower latency, lag, and power consumption

## Slide 10: Bluetooth Vulnerabilities
Attacks – Mitigations: security updates
  Bluejacking – send out message to nearby phones (nuisance) [14]
  Bluesnarfing - pushes a “get” request for files with a known filename, even for phones in non-discoverable mode [20]
    Requires the 48-bit Bluetooth device name
  Bluebugging (Pairing Vulnerabilities) can control phone including phone, SMS messages and microphone
  Key negotiation downgrade: BIAS [18] and Key Negotiation of Bluetooth (KNOB) [19]
  Bluesmack [20] - crafted oversized packets to crash the device or create a DoS attack
Additional mitigations:
  Tracking – turn off BT
  Limit connectivity, Limit app permissions
Notes: Bluebugging attacker executes a specific command in the parser that allows full access to a victim’s phone to make phone calls, a phone acting as a bug, hence the name. Bluebugging can also send short message service (SMS) texts, read SMS messages stored on the phone, read and write contact list entries, alter phone service parameters, connect to the Internet, forward calls, and more

## Slide 11: Zigbee
Notes: Medical: https://www.science.smith.edu/~jcardell/Courses/EGR328/Readings/Zigbee&HealthCare.pdf

## Slide 12: Zigbee
Low-cost, low-power wireless used to monitor and manage devices including:
  IoT devices
  Automated sensors
  Industrial automation
  Healthcare (pacemakers, insulin pumps)
Radio frequency (2.4 GHz) with a range of about 10-100m
AES 128-bit encryption algorithm
Notes: 10-100 m comms

## Slide 13: Zigbee Vulnerabilities
Symmetric encryption key sniffing [24-25]
DoS
  End-device sabotage attack – drain energy and cause power failures [25-26]
  Collision avoidance – (CSMA/CA) [23]
Replay attack – affect physical devices [26-27]
Mitigations:
  Do not broadcast keys unencrypted over network
    Add separate encryption key
  Rotate keys + secure key management
  Rate limiting (frequency and volume of polling requests)
  Cyber best practices
  More mitigations in [28]
Notes: Attacks mentioned in [28]
Communication interruption
Disconnection
Key leakage
Improper integrity check
Truncated packets

## Slide 14: Qi Wireless Charging Pad

## Slide 15: Qi
Used to charge handheld devices, home appliances, and other small electronics
  Standard maintained through the Wireless Power Consortium
  Current version 1.3. Version 2.0 specs behind paywall.
Frequently available for use at:
  Airports
  Restaurants
  Shopping malls

## Slide 16: Qi Vulnerabilities
Hijacking Attack [23,39]
  Denial of Charge
  Slow or excessive charging (explosion)
Eavesdropping Attack
  Able to determine / create signatures for active apps running:
    EX: Clash of Clans is running in the background
    Using YouTube
    Receiving a call or a text message
  Device tracking [32-38]
    Use Qi identifier to track individual device
    Create location-specific ads
    Subtle differences at the manufacturer-level (QID) [35-38]
Recommended mitigations [67-69] (not in protocol):
  Sliding window-based anomaly detection mechanisms
  Dynamic switching of amplitude/frequency to mitigate eavesdropping attacks
  Encrypting information (device ID, charging state, control info) [29,66]

## Slide 17: Li-Fi
Notes: R/Tx: https://www.hyperiontechs.com/product-category/devtools/lifi-devtools/
Receiver dongle: https://lifi.co/lifi-product/lifimax-flex/
Access point: https://terraferma.com/products/industrial-lifi-access-point-ap/#specs

## Slide 18: Li-Fi
Newer / faster wireless transmission than Wi-Fi
Uses light and a transceiver for communication
  Bidirectional, Full Duplex, High Speed, IP Addresses
Uses include low-infrastructure communications
  Disaster relief (FEMA, IEEE MOVE trucks?)
  Car headlights
  Airplane internet access
  Underwater applications
No RF – harder to detect
Notes: Use this as slide setup example

## Slide 19: Li-Fi Vulnerabilities
Transmission-level attacks [40-42]:
  Interference / DoS (physical block or flood with light)
  System fraud because of poor protections on the Li-Fi tags [45-46]
  Eavesdropping
    A gap between a door and the floor
    Others in same area with receiver in confined space
Mitigations:
  Physically shield light / limit access
  Dynamic ID updates on Li-Fi dongles [70]
  Authentication and handover protocols [71]
Notes: Interference – physical block or flood with light
Processing and Transmission Level Attacks, Input Level Attacks, Back-End Attack (especially for DoS) and Enrollment Attack. Transmission-level attack include eavesdropping and interference [40], [41]

## Slide 20: Survey Paper
RFID
  Close range wireless communication
  Tracking application
Bluetooth
  IoT Communication
  Many patched vulnerabilities
ZigBee
  Medium-Close range wireless communication
  Smart home application: Low power, long life
Qi
  Charging protocol
  Most applications include small handheld devices
Li-Fi
  Light and transceiver as a form of communication
  Similar application to WiFi

## Slide 21: Conclusion
Each technology has use case; strengths and weaknesses
Need to be aware before and during deployment of side-channel vulnerabilities and mitigations
Repeated advice across protocols is…
Use cybersecurity best practices:
  Install patches / updates
  Secure key management
  Security audits
  Technology-specific best practices

## Slide 22: Questions?
Dr. Shannon Beck
Shannon.Beck@afacademy.af.edu
Dept of Computer and Cyber Sciences